## Slide 1
TOPIC
High-Voltage Shore Connections: Technology, Regulations, Standards and Business Cases
By:
Cadet Anubhav Kumar, Cadet Ankit Kumar Singh & Cadet Sudama Kumar
TRANSTECH ’14
Sub Themes:
High Voltage Applications in Industries and Transportation
Marine Engineering & Research Institute, Indian Maritime University-Mumbai Campus, Mumbai

## Slide 2
Shore connection technology
Shore-side technology
Enabling the vessel’s power supply
A transformer for each ship’s power supply
Switchgear equipment such as breaker and dis connector for each ship’s power supply
An automated earthing switch for each ship’s power supply
A frequency converter, if power frequency needs to be stepped up from 50 Hz to 60 Hz or, vice-versa, stepped down.
Communications equipment to link the ship and shore
Protection relays in order to assure safety for cable-handlers

## Slide 3
What a Transformer does?
The transformer serves two purposes :
It provides galvanic separation (a non-metallic direct connection between the onshore power supply grid and the ship’s internal system), so that an earthing fault in the ship will not endanger the land grid or vice-versa.
The transformer steps down the voltage supply from a voltage level optimized for distribution (20 kilovolts, for example) to one of the two voltage levels standardised for shore-based power connections: 11 or 6.6 kilovolts.
50 Hz quay-side transformer in port

## Slide 4
2. Why do we need Switch gear equipment and Automated Earthing?
1. This switch ensures that there is no power in the cables between the ship and shore, while they are being handled and connected.
2. As the highest area of risk associated with shore-based power connections is injury to personnel manipulating the cables and systems, this system is critical.
3. Communications equipment :
Allowing personnel on land to coordinate the connection of cables .
And synchronizing the electrical load to the ship and off again.
This can be arranged by two computers – one on the ship and one on shore – with Ethernet communication and a fiber optic line incorporated in the cable connection.

## Slide 5
4. Use of Static Frequency Converter :
The majority of ships operate with 60 Hz supply, whereas local power grids in many parts of the world use 50 Hz. As a result, most shore-based power connections will require a frequency conversion.
Static frequency converters provide an economic solution to connect any ship to any grid independent of the required frequency.
Depending on the port’s layout, a centralized solution with one converter may serve multiple ships and berths.
These converters can fit into any substation building or container because of their small footprint.

## Slide 6
Medium-sized centralized solution with one or more converters in order to provide power to
quay-side transformers

## Slide 7
b) Ship-side technology
The Shore Connection System is arranged with the Shore Connection Panel located outside the main switchboard room with cable connectors mounted in the front. An onboard transformer steps down the power from high to low voltage.

## Slide 8
Contd….
The shore connection panel contains
A circuit breaker,
A protection relay,
The physical electrical connection (plugs and grounding cable) and
A control interface with the ship’s integrated automation system, or power management system.
These systems allow the incoming power to be synchronized with the ship’s diesel auxiliary engines before the load is transferred.
On ships that use conventional mechanical propulsion , the ship’s low-voltage auxiliary power system – typically 400 to 690 volts – requires a transformer to receive the 11 kV or 6.6 kV power supply from shore.

## Slide 9
Pros & Cons Of Shore Based Electricity
It is difficult to decide on long - term return on investment because of fluctuations in regulations and prices of HFO.
The production of electricity at shore can easily be optimized and made environmentally friendly as number of producers are reduced.
There is an advantage of jurisdiction for shore-based power supply i.e. it enables ports to establish a more efficient and powerful overall electrical supply as a utility.
Use frequency converter provides both a stabilizing effect on the local grid and an improved power factor.

## Slide 10
6. Shore-based power supply has an advantage to other emissions abatement technologies in that it reduces both noise and vibration in port areas.
7. Finally, shore-based power supply is easily scalable; infrastructure investments last for decades with relatively little maintenance, and long-term revenues.
8. Safety and efficiency concerns in port operations cannot be neglected in a study of shore based power supply. e.g. container terminals, with large, rolling gantry cranes, there are issues about the placement of cables and shore-side infrastructure.
9. In ports, space constraints again creates difficulty in installation activities.
Contd….

## Slide 11
Standardization of high-voltage shore connection systems
The four bodies that standardize shore connection regulations are :
International Electro technical Commission (IEC)
International Organization for Standardization (ISO)
International Maritime Organization (IMO)
The final authority – the Institute of Electrical and Electronics Engineers (IEEE)
The standards made applies to the specification, installation and testing of high-voltage shore connection systems and plants and addresses:
The high-voltage shore distribution system,
The shore-to-ship connection,
Transformers,
Ship distribution systems, and
Control, monitoring, interlocking and power management systems.

## Slide 12
The power needs and capacities of ships differ so much that a single standard would be unfeasible.
As a result, the standards work eventually settled on four separate, but linked, standards –
For Ro-Ro ships,
For container ships,
For cruise ships and
For tankers.
There are two main standard voltages for connection – 11 kilovolts and 6.6 kilovolts.
Contd….

## Slide 13
Business Case Arguments
Ship owners point of view :
For cruise ship owners transiting major cruise terminals on the US west coast (where environmental awareness is high and many ports are equipped for shore-based power), the business case is more positive for investing in the ship-board infrastructure.
To container ship owners that call at dozens of ports (most of which lack shore-based connections), the business case is obviously less rosy.
Ships with high power demands, such as cruise ships, LNG carriers, refrigerated ships and ferries, have a clearer business case than ships with smaller power demands.
The former are also frequently diesel-electric powered, which enables ship installation without a large and costly extra shipboard transformer.

## Slide 14
Thank you
Any Doubts?